Protocol for the RS485 communication

For the sake of speed there are two types of commands, firstly there needs to be a high speed command to ensure that all LED controllers can get updated as quickly as possible.

[Update][LED1][LED2][LED3][LED4][LED5]

[Update] will have the value 0xFE, however this will be ignored if in between a [Start] and [End]. If this value is detected it will be assumed that the next 5 bytes are for each of the LED strips, each device will be aware of it's own ID value and will only process the correct byte. The value of [LEDx] will correspond to a lookup table of up to 255 24 bit colour codes with value 0 being reserved for no colour similarly any unrecognised colour code will produce no colour.

However any other commands will not need to be processed quite so quickly, these will follow the much more rigid structure dictated below.

[Start][Addr][Cmd][Len][Data(0)]...[Data(Len-1)][End]

[Start] has the value 0xFC.
[Addr] will be the ID of the device you are trying to communicate with – 0x00 will be broadcast.
[Cmd] will be the command you wish the device to execute.
[Len] will be the number of data bytes in this command.
[Data(x)] will be data byte number x.
[End] has the value of 0xFD.

Commands:
Value	Can be broadcast	Description
0x01	Yes	Set update speed, contains a uint16 specifying the update speed in ms.
0x02	No	Get update speed, no data. Get the current update speed of the specified device. Device will return uint16 specifying update speed in ms.
0x03	No	Check Presence, no data. Device will reply with no data if it exists.
0x04	Yes	Reset, no data. Will clear all LED's and reset the buffers to empty.

Colour Codes:
Byte	Colour
0x00	No LED
0x01	0xFF0000
0x02	0x00FF00
0x03	0x0000FF